## Slide 1: Analog & Digital Signals
Course Code: COE 3201
Dept. of Computer Engineering
Faculty of Engineering
Lecture No: | 3 | Week No: | 3 | Semester: | 
Lecturer: |  |  |  |  | 
Course Title: Data Communication

## Slide 2: Lecture Outline
Analog and Digital Data
Analog and Digital Signals
Time and Frequency Domains
Composite Signal
Bandwidth
Transmission Impairment
Signal-to-Noise Ratio (SNR)

## Slide 3: Analog and Digital Data
Data can be
  Analog
  Digital
Analog data  information that is continuous
  Example: sounds made by a human voice
Digital data  information that has discrete states
  Example: data stored in computer memory (Os and 1s)

## Slide 4: Analog and Digital Signals
Like the data they represent, signals can be either
  Analog
  Digital
Analog signals can have an infinite number of values in a range
Digital signals can have only a limited number of values

## Slide 5: Periodic and Nonperiodic Signals
Both analog and digital signals can take one of two forms:
  Periodic
  Nonperiodic  Refer to as aperiodic, prefix a in Greek means "non“
Periodic signal
  Completes a pattern within a measurable time frame, called a period, and
  Repeats that pattern over subsequent identical periods
Completion of one full pattern is called a cycle
Nonperiodic signal changes without exhibiting a pattern or cycle
Both analog and digital signals can be periodic or nonperiodic
Commonly use: periodic analog signals (need less bandwidth) and nonperiodic digital signals (can represent variation in data)

## Slide 6: Periodic Analog Signals
Periodic analog signals can be classified as
  Simple or
  Composite
Simple periodic analog signal cannot be decomposed into simpler signals  a sine wave
Composite periodic analog signal is composed of multiple sine waves
Fig: Simple signal
Fig: Composite signal

## Slide 7: Sine Wave
Sine wave is the most fundamental form of a periodic analog signal
Its change over the course of a cycle is smooth and consistent, a continuous, rolling flow
A sine wave can be represented by three parameters: the peak amplitude, the frequency, and the phase
Fig: Sine wave

## Slide 8
Peak Amplitude
  is the absolute value of its highest intensity
  proportional to the energy it carries
Frequency refers to the number of periods in 1 s. Note that period and frequency are just one characteristic defined in two ways.
Period is the inverse of frequency, and frequency is the inverse of period
Frequency is formally expressed in Hertz (Hz), which is cycle per second.

## Slide 9: Units of period and frequency
Example:

## Slide 10: Phase
Phase describes the position of the waveform relative to time 0
Phase is measured in degrees or radians [360° is 2π rad; 1° is 2π/360 rad, and 1 rad is 360/(2π)]
A phase shift of 360° corresponds to a shift of a complete period;
A phase shift of 180° corresponds to a shift of one-half of a period
A phase shift of 90° corresponds to a shift of one-quarter of a period
Fig: Three sine waves with the same amplitude and frequency, but different phases

## Slide 11: Wavelength
Wavelength is another characteristic of a signal traveling through a transmission medium
Wavelength binds the period or the frequency of a simple sine wave to the propagation speed of the medium

## Slide 12: Time and Frequency Domains
Time-domain plot
  Shows changes in signal amplitude with respect to time  amplitude-versus-time plot
  Phase is not explicitly shown on a time-domain plot
Frequency-domain plot
  To show the relationship between amplitude and frequency
  Concerned with only the peak value and the frequency
  Changes of amplitude during one period are not shown

## Slide 13: Composite Signal
A single-frequency sine wave is not useful in data communications
Need to send a composite signal  a signal made of many simple sine waves
According to Fourier analysis, any composite signal is a combination of simple sine waves with different frequencies, amplitudes, and phases.
If the composite signal is periodic, the decomposition gives a series of signals with discrete frequencies
If the composite signal is nonperiodic, the decomposition gives a combination of sine waves with continuous frequencies

## Slide 14: Periodic Composite Signal: can be decomposed into a number of signals with discrete frequencies in the frequency domain
Fig: Decomposition of a composite periodic signal in the time and frequency domains
Fig: A composite periodic signal
Nonperiodic Composite Signal: In a time-domain representation of this composite signal, there are an infinite number of simple sine frequencies

## Slide 15: Bandwidth
The range of frequencies contained in a composite signal is its bandwidth
The bandwidth of a composite signal is the difference between the highest and the lowest frequencies contained in that signal
For example, if a composite signal contains frequencies between 1000 and 5000, its bandwidth is 5000 − 1000, or 4000
Fig: The bandwidth of periodic and nonperiodic composite signals

## Slide 16: Transmission Impairment
Signals travel through transmission media, which are not perfect
The imperfection causes signal impairment
This means that the signal at the beginning of the medium is not the same as the signal at the end of the medium
Three causes of impairment are-
  attenuation,
  distortion, and
  noise

## Slide 17
Attenuation means a loss of energy.
When a signal, simple or composite, travels through a medium, it loses some of its energy in overcoming the resistance of the medium.
Fig: Attenuation

## Slide 18
Decibel
  To show that a signal has lost or gained strength, engineers use the unit of the decibel.
  The decibel (dB) measures the relative strengths of two signals or one signal at two different points.
Variables P1 and P2 are the powers of a signal at points 1 and 2, respectively.
Note that the decibel is negative if a signal is attenuated and positive if a signal is amplified.
Example: The loss in a cable is usually defined in decibels per kilometer (dB/km). If the signal at the beginning of a cable with −0.3 dB/km has a power of 2 mW, what is the power of the signal at 5 km?

## Slide 19
Distortion means that the signal changes its form or shape and can occur in a composite signal.
Each signal component has its own propagation speed through a medium and, therefore, its own delay in arriving at the final destination
Differences in delay may create a difference in phase if the delay is not exactly the same as the period duration.

## Slide 20
Noise is another cause of impairment.
Several types of noise,
  Thermal noise  random motion of electrons in a wire, which creates an extra signal not originally sent by the transmitter
  Induced noise comes from sources such as motors and appliances
  Impulse noise  that comes from power lines, lightning, and so on

## Slide 21: Signal-to-Noise Ratio (SNR)
To find the theoretical bit rate limit, we need to know the ratio of the signal power to the noise power. The signal-to-noise ratio is defined as
SNR is actually the ratio of what is wanted (signal) to what is not wanted (noise).
Because SNR is the ratio of two powers, it is often described in decibel units, SNRdB, defined as
Example: The power of a signal is 10 mW and the power of the noise is 1 μW; what are the values of SNR and SNRdB

## Slide 22
Books
Forouzan, B. A. "Data Communication and Networking. Tata McGraw." (2005).

## Slide 23
References
1. Prakash C. Gupta, “Data communications”, Prentice Hall India Pvt.
2. William Stallings, "Data and Computer Communications”, Pearson
3. Forouzan, B. A. "Data Communication and Networking. Tata McGraw." (2005).